## Slide 1: Long read sequencing
Next-Generation-Sequencing Analysis
09-01-2025
Frederikke Byron Pedersen MscEng
Clinical Scientist & PhD Student
Department of Clinical Immunology
The University Hospital of Copenhagen, Rigshospitalet
Frederikke.Byron.Pedersen@regionh.dk

## Slide 2: About the presenter
Part time PhD student (Public Health and Epidemiology, KU), part time Clinical Scientist at Rigshospitalet since 2024
Worked fulltime at the Department of Clinical Immunology at Rigshospitalet from 2021-2023
Worked at Nanopore Technologies from 2019-2021
Graduated from DTU in 2019, master in Biotechnology
Worked with longread sequencing since 2018, and short reads since 2021
How to get in touch?
Frederikke.Byron.Pedersen@regionh.dk

## Slide 3: Sequencing Techniques: An overview
Sanger Sequencing
(First generation sequencing)
Next generation Sequencing
Second generation sequencing
Third generation sequencing
Illumina
Ion Torrent
PacBio
Nanopore

## Slide 4: Quiz
5 multiple choice questions
Note your answers on a piece of paper or laptop

## Slide 5: Question 1: What is the longest read that can be obtained using Nanopore Sequencing? Note, not average read length
25kb
100kb
10kb
No limit

## Slide 6: Question 2: What is the longest read that can be obtained using PacBio Sequencing? Note, not average read length
25kb
100kb
10kb
No limit

## Slide 7: Question 3: What is phasing?
To introduce something in stages over a particular period of time
Phasing is the rhythmic equivalent of cycling through the phase of two waveforms as in phasing
The process of statistical estimation of haplotypes from genotype data
All of the above

## Slide 8: Question 4: What is one of the main advantages of Long Read Sequencing?
Haplotyping and SVs are easier resolved
Cheaper and Faster
Higher quality/Q-Score
All of the above

## Slide 9: Question 5: Which sequencing platform is the best?
PacBio
Nanopore
Illumina
It depends on what you want to do

## Slide 10: Why Long Read Sequencing?
Assembly
Phasing/Haplotyping
Plasmids
Methylation
Structural Variants (SVs)
Large Repetitive Regions
Plant genomes
More?
Disclaimer:
Each of these could fill an entire lecture. The next slides will give a quick overview of each.

## Slide 11: Assembly with reference genome
https://www.phgfoundation.org/briefing/clinical-long-read-sequencing
Another thing that is much easier with Long Reads is De novo assembly

## Slide 12: Phasing
https://www.pacb.com/blog/ploidy-haplotypes-and-phasing/

## Slide 13: Assembly/Haplotyping, diploid (Human)
A
B
C
D
B
E
Maternal
Paternal
Short read Sequencing
Assemblies
A
B
C
D
B
E
A
B
E
D
B
C
What assemblies will we get?

## Slide 14: Assembly/Haplotyping, diploid (Human)
A
B
C
D
B
E
Maternal
Paternal
Long read Sequencing
Assembly
A
B
C
D
B
E

## Slide 15: Assembly/Haplotyping, diploid (Human)
A
B
C
D
B
E
Maternal
Paternal
Ultra
Long read Sequencing
Assembly
A
B
C
D
B
E

## Slide 16: Assembly/Haplotyping, hexaploid (Plant)
A
B
C
D
B
E
Short read Sequencing
Would short reads ever be able to properly phase it?
A
D
C
D
B
A
B
C
D
D
B
C

## Slide 17: Phasing – A real life example, using Illumina sequencing
Over 2kb to nearest heterozygote position
Our analysis program warns us that this is a new DPB1 type called DPB1*13:New

## Slide 19
Upon re-running the sample, it now calls it a DPB1*11:New

## Slide 20
What happened?

## Slide 21: Plasmids
Why use long reads for Plasmids sequencing?
Plasmids can be up to several hundred kb
It is important to be able to know which plasmid an antibiotic resistance gene is on, to be able to track it.

## Slide 22: Methylation, what is it, and is it useful information?
Ambrosi et al. 2017 ”Dynamics and context dependent roles of DNA Methylation”
Briefly: gene expression regulation. Among other things, it influences what type of cell a naïve cell becomes, by determining which genes are expressed.

## Slide 23: Structural Variants (SVs)
https://www.nature.com/articles/s41698-021-00155-6

## Slide 24: Repetitive regions and their challenge
Shown is the GC bias in Illumina reads from a 400-bp fragment library amplified using the standard PCR protocol (Phusion HF, short denaturation) on a fast-ramping thermocycler (red squares), Phusion HF with long denaturation and 2M betaine (black triangles), AccuPrime Taq HiFi with long denaturation and primer extension at 65°C (blue diamonds) or 60°C (purple diamonds)
https://genomebiology.biomedcentral.com/articles/10.1186/gb-2011-12-2-r18
Old overview, but still illustrates the issues with short read sequencing
Repetitive sequences, why are they a problem when sequencing?:
High or low GC regions are hard to amplify
DNA fragmentation is not random
Hard to assemble with short reads, if the repetitive region becomes larger than 100bp. Tandem repeats can be up to 1,7Mbp in size
To overcome this, use sequencing methods that do not require PCR and fragmentation, and produces long reads.

## Slide 25: The two main Long Read Sequencing technologies
Not to scale

## Slide 26: Nanopore sequencing
Source: Nature.com Nanopore sequencing technology, bioinformatics and applications

## Slide 27: Library preparation: highlighted methods
Ligation Sequencing Kit
Rapid Sequencing Kit
Both have barcoding options up to 96, and there are many other library preparation methods, including for RNA and cDNA
https://nanoporetech.com/products/prepare/dna-library-preparation

## Slide 28: Biggest hurdle with Nanopore: Homopolymers

## Slide 29
Real life example, typing of HLA in a Stem Cell Donor
Suddenly random errors become systematic base calling errors

## Slide 30: Duplex basecalling to overcome homopolymers?
https://nanoporetech.com/resource-centre/video/ncm22/advances-in-duplex-basecalling
So, better Q/Phred score, but lower output. Only ~20% of the reads are duplex, and this does not work with barcoded reads (yet)
What base should
this have been?

## Slide 31: PacBio (HiFi)
https://www.pacb.com/technology/hifi-sequencing/

## Slide 32: PacBio Sequencing

## Slide 33: Library preparation
SMRTbell® prep kit 3.0
Preparing multiplexed amplicon libraries using SMRTBell prep kit 3.0

## Slide 34: Biggest hurdles with Pacbio HiFi/Revio
Limited read length
Requires shearing or amplification, which may lead to low coverage of high or low GC rich areas
Fixed sequencing time for a SMRT cell
It’s large

## Slide 35
The enrichment strategies can be used on all sequencing platforms, except Adaptive Sampling, which requires the use of Nanopore’s ability to flick out a read using the positive and negative charge.
https://www.nature.com/articles/s41576-023-00600-1

## Slide 36: My experiences with Long Read Sequencing
Plasmids, tracking of antibiotic resistance – SSI
Cas9 Mediated Enrichment – Oxford Nanopore Technologies (ONT)
Leukemia panel (AML), one diagnostic tool for all types of AML – ONT
Covid-19 test – ONT
De Novo Assembly of viral DNA in metagenomic samples, getting a consensus/reference sequence for new variants/virus – ONT
HLA typing – The University Hospital of Copenhagen, Rigshospitalet

## Slide 37: Comparison of the 3 major players in sequencing
 | Illumina (MiSeq) | Nanopore (MinION) | PacBio (Revio/SMRT)
Maximum read length | 600bp | None (record >4mb) | 25kb
Cost per instrument | $128,000 | $1,000* | $779,000
Q score | ~Q40 (Min Q30) | ~Q20 (Personal experience say it’s Q15) | ~Q30 (Min Q20)
Minimum Run Time | 4h (1x36bp) 56h (2x300bp) | None | 24h
Methylation? | No | Yes | Yes
Direct RNA Seq | No | Yes | No
Mobile | No | Yes | No
Reusable flow cells | No | Yes | No
*lease of the instrument

## Slide 38: Quiz
Same questions, compare your answers to those at the start of the lecture. Have they changed?

## Slide 39: Question 1: What is the longest read that can be obtained using Nanopore Sequencing? Note, not average read length
25kb
100kb
10kb
No limit

## Slide 40: Question 2: What is the longest read that can be obtained using PacBio Sequencing? Note, not average read length
25kb
100kb
10kb
No limit

## Slide 41: Question 3: What is phasing?
To introduce something in stages over a particular period of time
Phasing is the rhythmic equivalent of cycling through the phase of two waveforms as in phasing
The process of statistical estimation of haplotypes from genotype data
All of the above

## Slide 42: Question 4: What is one of the main advantages of Long Read Sequencing?
Haplotyping and SVs are easier resolved
Cheaper and Faster
Higher quality/Q-Score
All of the above

## Slide 43: Question 5: Which sequencing platform is the best?
PacBio
Nanopore
Illumina
It depends on what you want to do

## Slide 44: Questions?